## Slide 1: 一個策略選擇，如何變成可核對的端點能量？
MECH · 01
只改一個地方
REST_DURING_GAP
WAIT
SLEEP
同一個情境、只換選擇
方向先當假設
證據決定結論
狀態與事件，是策略通往證據的橋
WAIT
SLEEP
狀態時間
+ WAKE ?
功率 × 時間
endpoint
J
服務先判
verdict
WAIT = awake idle；下一次決策不需 WAKE
SLEEP = low-power rest；下一次 active 多 WAKE energy + latency
判讀順序：service / deadline / freshness → endpoint energy
Null evidence change = consequential gate FAIL
只有動畫變化，不算策略造成後果
SIMULATED TEACHING DATA / NOT LIVE / NOT MEASURED / NOT CANONICAL-PARITY-VERIFIED

## Slide 2: 短窗口決策：服務、佇列與能量
DECIDE · 02
只改一個值
BATCH_SIZE
批次大小
或
URGENT_MARGIN_S
緊急提前量
同一 mission contract 不變
batching vs urgency
服務條件先選 action
1
CONTACT OPEN?
NO
SLEEP
YES
2
URGENT DUE?
YES
SEND_URGENT
NO
3
PACING GAP?
YES
WAIT / SLEEP
NO
4
QUALITY READY?
YES
FLUSH_BATCH / ONE
NO
WAIT
EVIDENCE GATE
先凍結
baseline
candidate
one evidence-based revision
FREEZE
withheld
SERVICE
deadline / freshness
MECHANISM
queue / retry
STATE
wake / TX
ENERGY
endpoint J
服務失敗不得用 bit/J 蓋過；FREEZE 後的 withheld 不再 retune
SIMULATED TEACHING DATA / NOT LIVE / NOT MEASURED / NOT CANONICAL-PARITY-VERIFIED

## Slide 3: 能量變好，不等於系統成功
CLAIM · 03
Prediction ≠
Saving
先通過服務
再談能量
≠
endpoint bit/J
只在同一 boundary 比
證據鏈不能跳步
IDENTITY
同情境
scenario / seed
SERVICE
服務門檻
deadline / fresh
MECHANISM
機制證據
queue / state
ENDPOINT J
能量分解
same boundary
CLAIM
有界結論
conditional
同 scenario / policy / case / seed / freeze，才有資格比較下一步
可辯護的結論句
固定 scenario / policy / case 同一 endpoint energy boundary mechanism → evidence → service verdict 只提出 conditional claim
COMPLETE
INCOMPLETE
identity match
identity mismatch
service pass
service fail
trace found
trace missing
匯入或 replay identity 失敗：保留 prior state / same-scenario fallback；不可捏造 KPI 或完成狀態
SIMULATED TEACHING DATA / NOT LIVE / NOT MEASURED / NOT CANONICAL-PARITY-VERIFIED